## Slide 1: Process Design Flowsheet

## Slide 2: Flowsheet Block
CO
MN
NO
REACTOR 1
SEPARATION 1
Recycle reactant
REACTOR 2
SEPARATION 2
Ethylene Glycol
Side products
H2
Flowsheet 1
Flowsheet 2
CO
MN
NO
REACTOR 1
SEPARATION 1
REACTOR 2
SEPARATION 2
Ethylene Glycol
Side products
H2
2 distillation column
Flash tank
Better separation
More DMO
More complicated
More purchase
Less energy usage
Worse separation
Less DMO
Simpler
Less purchase
More energy usage

## Slide 3: Process Flow Diagram Flowsheet 1
H2

## Slide 4: Process Flow Diagram Flowsheet 2
H2

## Slide 5: Reactor 1 : producing DMO
Flowsheet 1
Flowsheet 2
8000 kg/hr MN
1000 kg/hr NO
6000 kg/hr CO
-174.3℃, 5 bar
16294.5 kg/hr
100w% CO
129℃, 5 bar
31294.5 kg/hr
24.66w% DMO
59.54w% CO
15.73w% NO
0.07w% MN
Temp : 129℃
Pressure : 5 bar
Duty: 4710.65 kW
Volume: 1597.86 L
Parameter
Mass Balance
129℃, 5 bar
11990 kg/hr
65.31w% DMO
0.21w% CO
34.02w% NO
0.46w% MN
8150 kg/hr MN
100 kg/hr NO
3740 kg/hr CO
Temp : 129℃
Pressure : 5 bar
Duty: 12635.2 kW
Volume: 254.38 L
Parameter
Mass Balance
 | In (kg/hr) | Out (kg/hr)
MN | 8000 | 21.91
NO | 1000 | 4922.62
CO | 22294.5 | 18632.75
DMO | - | 7717.22
Conversion = 1
Selectivity = 0.5
Reactor Yield = 1
 | In (kg/hr) | Out (kg/hr)
MN | 8150 | 55.154
NO | 100 | 4079
CO | 3740 | 25.179
DMO | - | 7830.67
Conversion = 0.99
Selectivity = 0.5
Reactor Yield = 1

## Slide 6: Separation 1: separating DMO
Flowsheet 1
6
Condenser duty: -4175.38 kW
Reboiler duty:
-6031.5 kW
NTS: 16 (feed stream: 4)
RR (mole): 5
-174.3℃, 5 bar
16294.5 kg/hr
100w% CO
129℃, 5 bar
31294.5 kg/hr
24.66w% DMO
59.54w% CO
15.73w% NO
0.07w% MN
-157.49℃, 5 bar
15000.02 kg/hr
51.46w% DMO
15.59w% CO
32.82w% NO
0.14w% MN
137.513℃, 1 bar
7835.55 kg/hr
98.51w% DMO
0.26w% MN
1.23w% NO
Condenser duty: 1236.95kW
Reboiler duty:
2076.19kW
NTS: 21 (feed stream: 16)
RR (mole): 0.45
Flowsheet 2
-182.59℃, 1 bar
7164.68 kg/hr
32.64w% CO
67.36w% NO
85℃, 1.15 bar
7797.82 kg/hr
96.16w% DMO
0.01w% CO
3.82w% NO
85℃, 1.15 bar
4192.18 kg/hr
7.92w% DMO
0.58w% CO
90.21w% NO
1.29w% MN
129℃, 5 bar
11990 kg/hr
65.31w% DMO
0.21w% CO
34.02w% NO
0.46w% MN
-16119.2 kW
-200.79 kW
vapor fraction (mole): 0.64
DMO separated: 7718.8 kg/hr (100%)
DMO separated: 7498.38 kg/hr (95.76%)
CO
NO
DMO
Light key
Heavy key

## Slide 7: Reactor 2: producing EG
Flowsheet 1
102.31℃, 1 bar
4201 kg/hr
6.74w% H2
91.87w% DMO
1.15w% NO
Split frac: 0.5
-858.92 kW
200℃, 16 bar
6 m, 100 tubes, 0.02 m diameter, 14 kg catalyst
-419.15 kW
241℃, 24 bar
6 m, 500 tubes, 0.02 m diameter, 923 kg catalyst
200℃, 16 bar
4201 kg/hr
6.71w% H2
90.98w% DMO
0.24w% MeOH
0.68w% MG
241℃, 24 bar
4201 kg/hr
4.68w% H2
50.18w% DMO
16.41w% MeOH
17.45w% MG
9.89w% EG
Chart: 1st reactor
| 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221
 | 415.3288 | 415.3232 | 415.3162 | 415.3095 | 415.3037 | 415.2966 | 415.2895 | 415.2825 | 415.2754 | 415.268 | 415.2601 | 415.2524 | 415.2443 | 415.2364 | 415.2281 | 415.2197 | 415.2105 | 415.202 | 415.194 | 415.1847 | 415.1749 | 415.1649
Chart: 2nd reactor
| 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239 | 240 | 241 | 242
 | 336.4642 | 344.9589 | 353.5872 | 362.2847 | 370.9499 | 379.4122 | 387.4063 | 394.5051 | 400.6016 | 407.9759 | 415.3288 | 129.7911
Sensitivity Test
Chart: Temperature Profile
| 0 | 0.6 | 1.2 | 1.8 | 2.4 | 3 | 3.6 | 4.2 | 4.8 | 5.4 | 6
1st reactor | 200 | 199 | 199 | 199 | 199 | 199 | 199 | 199 | 199 | 199 | 199
2nd reactor | 241 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85
Chart: Pressure Profile
| 0 | 0.6 | 1.2 | 1.8 | 2.4 | 3 | 3.6 | 4.2 | 4.8 | 5.4 | 6
 | 16 | 14.5 | 13 | 11.5 | 10 | 8.5 | 7 | 5.5 | 4 | 2.5 | 1
 | 24 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 8: Reactor 2: producing EG
Flowsheet 2
81.71℃, 1.15 bar
4185.16 kg/hr
6.84w% H2
89.58w% DMO
3.56w% NO
200℃, 16 bar
4185.16 kg/hr
6.81w% H2
88.69w% DMO
0.24w% MeOH
0.68w% MG
244℃, 26 bar
4185.16 kg/hr
4.41w% H2
38.5w% DMO
19.29w% MeOH
23.70w% MG
10.52w% EG
Split frac:0.5
-755.05 kW
200℃, 16 bar
6 m, 100 tubes, 0.02 m diameter, 14 kg catalyst
-750.69 kW
244℃, 26 bar
6 m, 500 tubes, 0.02 m diameter, 923 kg catalyst
Chart: 1st reactor
| 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216
 | 390.2884 | 390.2776 | 390.2679 | 390.2568 | 390.2454 | 390.2336 | 390.2221 | 390.2102 | 390.1974 | 390.1851 | 390.172 | 390.1587 | 390.1447 | 390.1315 | 390.1166 | 390.102 | 390.0871
Chart: 2nd reactor
| 223 | 224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239 | 240 | 241 | 242 | 243 | 244 | 245
 | 276.4499 | 283.4438 | 290.6207 | 297.9864 | 305.5466 | 313.308 | 321.2725 | 329.4423 | 337.8136 | 346.3763 | 355.1071 | 363.9647 | 372.8747 | 381.7157 | 390.2887 | 398.2638 | 405.0601 | 410.128 | 417.4508 | 424.926 | 432.474 | 440.097 | 161.7026
Sensitivity Test
Chart: Temperature Profile
| 0 | 0.6 | 1.2 | 1.8 | 2.4 | 3 | 3.6 | 4.2 | 4.8 | 5.4 | 6
1st reactor | 200 | 199 | 199 | 199 | 199 | 199 | 199 | 199 | 199 | 199 | 199
2nd reactor | 244 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85 | 26.85
Chart: Pressure Profile
| 0 | 0.6 | 1.2 | 1.8 | 2.4 | 3 | 3.6 | 4.2 | 4.8 | 5.4 | 6
 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16
 | 26 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 9: Reactor 2-Comparison
 | Flowsheet 1 | Flowaheet 2
Duty 1 (kW) | -858.92 | -755.05
Duty 2 (kW) | -415.15 | -750.69
EG produced (kg/hr) | 830.96 | 880.19
Conversion (DMO) | 0.45 | 0.57
Selectivity (DMO) | 0.45 | 0.39
Yield (DMO) | 0.45 | 0.39
Conversion (H2) | 0.31 | 0.35
Selectivity (H2) | 0.16 | 0.14
Yield (H2) | 0.31 | 0.28

## Slide 10: Separation 2: Getting EG
Flowsheet 1
193.45℃, 1 bar
7571.91 kg/hr
5.19w% H2
55.68w% DMO
18.21w% MeOH
19.36w% MG
0.02w% EG
1.27 w% NO
Reb duty: 7.06 MW
Cond duty: -7.47 MW
NTS: 25
(feed stream: 18)
RR (mole): 2
205.23℃, 1 bar
830 kg/hr
100w% EG
H2
NO
CH3OH
MG
DMO
EG
This is hard to separate
Interest compound
feed

## Slide 11
142.904℃, 1 bar
7490.2 kg/hr
4.93w% H2
42.85w% DMO
21.56w% MeOH
25.49w% MG
0.17w% EG
3.98w% NO
Reb duty: 11.63 MW
Cond duty: -12.28 MW
NTS: 30
(feed stream: 22)
RR (mole): 2
199.1℃, 1 bar
880 kg/hr
99w% EG
Separation 2: Getting EG
11
Flowsheet 2
H2
NO
CH3OH
MG
DMO
EG
This is hard to separate
Interest compound
feed

## Slide 12: Aspen Simulation Flowsheet 1
8000 kg/hr MN
1000 kg/hr NO
6000 kg/hr CO
H2 566.46 kg/hr
Reb duty: -6.03 MW
Cond duty: -4.17 MW
NTS: 16
(feed stream: 4)
RR (mole): 5
-174.3℃, 5 bar
16294.5 kg/hr
100w% CO
129℃, 5 bar
31294.5 kg/hr
24.66w% DMO
59.54w% CO
15.73w% NO
0.07w% MN
-182.59℃, 1 bar
7164.68 kg/hr
32.64w% CO
67.36w% NO
-157.49℃, 5 bar
15000.02 kg/hr
51.46w% DMO
15.59w% CO
32.82w% NO
0.14w% MN
137.513℃, 1 bar
7835.55 kg/hr
98.51w% DMO
0.26w% MN
1.23w% NO
NTS: 21
(feed stream: 16)
RR (mole): 0.45
Reb duty: 2.08 MW
Cond duty: 1.24 MW
129℃, 5 bar
4710.65 kW
1597.86 L
102.31℃, 1 bar
4201 kg/hr
6.74w% H2
91.87w% DMO
1.15w% NO
193.45℃, 1 bar
7571.91 kg/hr
5.19w% H2
55.68w% DMO
18.21w% MeOH
19.36w% MG
0.02w% EG
1.27 w% NO
241℃, 24 bar
4201 kg/hr
4.68w% H2
50.18w% DMO
16.41w% MeOH
17.45w% MG
9.89w% EG
Split fraction (mole): 0.5
-858.92 kW
200℃, 16 bar
6 m, 100 tubes,
D: 0.02 m, 14 kg cat
-415.15 kW
241℃, 24 bar
6 m, 500 tubes,
D: 0.02 m, 923 kg cat
Reb duty: 7.06 MW
Cond duty: -7.47 MW
NTS: 25 (feed stream: 18)
RR (mole): 2
200℃, 16 bar
4201 kg/hr
6.71w% H2
90.98w% DMO
0.24w% MeOH
0.68w% MG
205.23℃, 1 bar
830 kg/hr
100w% EG

## Slide 13: Aspen Simulation Flowsheet 2
25℃, 1 bar
100 kg/hr
25℃, 1 bar
8150 kg/hr
25℃, 5.17 bar
3740 kg/hr
-16119.2 kW
-200.79 kW
vapor fraction (mole): 0.64
85℃, 1.15 bar
7797.82 kg/hr
96.16w% DMO
0.01w% CO
3.82w% NO
85℃, 1.15 bar
4192.18 kg/hr
7.92w% DMO
0.58w% CO
90.21w% NO
1.29w% MN
129℃, 5 bar
11990 kg/hr
65.31w% DMO
0.21w% CO
34.02w% NO
0.46w% MN
20℃, 25.5 bar
572.51 kg/hr
81.71℃, 1.15 bar
4185.16 kg/hr
6.84w% H2
89.58w% DMO
3.56w% NO
Split fraction (mole): 0.5
-755.05 kW
200℃, 16 bar
6 m, 100 tubes, 0.02 m diameter, 14 kg catalyst
-750.69 kW
244℃, 26 bar
6 m, 500 tubes, 0.02 m diameter, 923 kg catalyst
129℃, 5 bar
12635.2 kW
254.38 L
142.904℃, 1 bar
7490.2 kg/hr
4.93w% H2
42.85w% DMO
21.56w% MeOH
25.49w% MG
0.17w% EG
3.98w% NO
Reb duty: 11.63 MW
Cond duty: -12.28 MW
NTS: 30
(feed stream: 22)
RR (mole): 2
199.1℃, 1 bar
880 kg/hr
99w% EG
200℃, 16 bar
4185.16 kg/hr
6.81w% H2
88.69w% DMO
0.24w% MeOH
0.68w% MG
244℃, 26 bar
4185.16 kg/hr
4.41w% H2
38.5w% DMO
19.29w% MeOH
23.70w% MG
10.52w% EG

## Slide 14: P&ID Diagram Flowsheet 2
Steam
Steam
222
Coolant
Steam
Steam

## Slide 15: P&ID Diagram Flowsheet 2
Steam
Steam

## Slide 16: Floor Plan
52 m
35 m
3552

## Slide 17: Economic Analysist

## Slide 18: Review Previous Presentation
Economic Potential: $6276.29
 | Flowsheet 1 | Flowsheet 2
Raw Material Cost | $16,749,675 | $4,508,443
Revenue | $674,300,000 | $652,100,000
Catalyst Cost | $673,466 | 
Total reactor purchase | $101,336 | 
Total reactor installment | $142,081 | 
Total Distillation Column Instalment | $400,183 | $112,581
Total Tray Instalment | $46,412 | $94,285
Total Reboiler instalment | $1,157,010 | $760,622
Total Condenser instalment | $136,429 | $107,906
Flash tank instalment | - | $107,906
Total Utility Cost | $13,247,673 | $24,734,910

## Slide 19: Distillation Column Cost – Flowsheet 1&2
Formula |  |  |  |  |  |  | 
 | Specification |  |  |  |  |  | Installed Cost
 | No of Stages | Diameter (ft) | Height (ft) | Fm | Fp | Fc | 
C1 | 16 | 2.4 | 33.07 | 1 | 1 | 1 | $35,403
C2 | 21 | 1.54 | 44.88 | 1 | 1 | 1 | $28,339
C3 | 20 | 3.18 | 42.52 | 1 | 1 | 1 | $58,726
Total |  |  |  |  |  |  | $122,468
Formula |  |  |  |  |  |  | 
 | Specification |  |  |  |  |  | Installed Cost
 | No of Stages | Diameter (ft) | Height (ft) | Fm | Fp | Fc | 
C1 | 16 | 2.4 | 33.07 | 1 | 1 | 1 | $35,403
C2 | 21 | 1.54 | 44.88 | 1 | 1 | 1 | $28,339
C3 | 20 | 3.18 | 42.52 | 1 | 1 | 1 | $58,726
Total |  |  |  |  |  |  | $122,468
Formula |  |  |  |  |  |  | 
 | Specification |  |  |  |  |  | Installed Cost
 | No of Stages | Diameter (ft) | Height (ft) | Fm | Fp | Fc | 
C1 | 30 | 5.61 | 66.14 | 1 | 1 | 1 | $154,515
Total |  |  |  |  |  |  | $154,515
Formula |  |  |  |  |  |  | 
 | Specification |  |  |  |  |  | Installed Cost
 | No of Stages | Diameter (ft) | Height (ft) | Fm | Fp | Fc | 
C1 | 30 | 5.61 | 66.14 | 1 | 1 | 1 | $154,515
Total |  |  |  |  |  |  | $154,515
Marshall and Swift (2020): 2171.6
Cost reference: Table A4 from James M. Douglas. (1988). Conceptual Design of Chemical Processes. McGraw-Hill Book Company.

## Slide 20: Reboiler Cost Flowsheet 1
Cost reference: Table A4 from James M. Douglas. (1988). Conceptual Design of Chemical Processes. McGraw-Hill Book Company.
Marshall and Swift (2020): 2171.6
Fc = (Fd + Fp) Fm
 | C1 | C2 | C3
Heat Duty (MW) | 6.0315 | 2.08 | 20.3836
 | 70.49 | 181.56 | 3385.89
 | 0 | 0 | 0
 | 2.81 | 2.81 | 2.81
 | 1.35 | 1.35 | 1.35
 | 3.79 | 3.79 | 3.79
Purchase Cost | $47,332 | $87,545 | $586,351
 | C1 | C2 | C3
Heat Duty (MW) | 6.0315 | 2.08 | 20.3836
 | 70.49 | 181.56 | 3385.89
 | 0 | 0 | 0
 | 2.81 | 2.81 | 2.81
 | 1.35 | 1.35 | 1.35
 | 3.79 | 3.79 | 3.79
Purchase Cost | $47,332 | $87,545 | $586,351
Total Purchase Cost: $721,228

## Slide 21: Reboiler Cost Flowsheet 2
Cost reference: Table A4 from James M. Douglas. (1988). Conceptual Design of Chemical Processes. McGraw-Hill Book Company.
Marshall and Swift (2020): 2171.6
Fc = (Fd + Fp) Fm
 | C1
Heat Duty (MW) | -11.8724
 | 2441.998
 | 0
 | 2.81
 | 1.35
 | 3.79
Installed Cost | $474,138
 | C1
Heat Duty (MW) | -11.8724
 | 2441.998
 | 0
 | 2.81
 | 1.35
 | 3.79
Installed Cost | $474,138

## Slide 22: Condenser Cost Flowsheet 1
Cost reference: Table A4 from James M. Douglas. (1988). Conceptual Design of Chemical Processes. McGraw-Hill Book Company.
Marshall and Swift (2020): 2171.6
Fc = (Fd + Fp) Fm
 | C1 | C2 | C3
Heat Duty (MW) | -6.03 | 2.08 | 26.48
 | 47.26 | 47.92 | 48.57
 | 0 | 0 | 0
 | 2.81 | 2.81 | 2.81
 | 0.85 | 0.85 | 0.85
 | 2.39 | 2.39 | 2.39
Installed Cost | $23,017 | $23,226 | $23,430
 | C1 | C2 | C3
Heat Duty (MW) | -6.03 | 2.08 | 26.48
 | 47.26 | 47.92 | 48.57
 | 0 | 0 | 0
 | 2.81 | 2.81 | 2.81
 | 0.85 | 0.85 | 0.85
 | 2.39 | 2.39 | 2.39
Installed Cost | $23,017 | $23,226 | $23,430
Total Purchase Cost: $69,673

## Slide 23: Condenser Cost Flowsheet 2
Cost reference: Table A4 from James M. Douglas. (1988). Conceptual Design of Chemical Processes. McGraw-Hill Book Company.
Marshall and Swift (2020): 2171.6
Fc = (Fd + Fp) Fm
 | C1
Heat Duty (MW) | -6.03
 | 181.05
 | 0
 | 2.81
 | 0.85
 | 2.39
Installed Cost | $55,106
 | C1
Heat Duty (MW) | -6.03
 | 181.05
 | 0
 | 2.81
 | 0.85
 | 2.39
Installed Cost | $55,106

## Slide 24: Flask Tank Cost Flowsheet 2
Cost reference: Table A4 from James M. Douglas. (1988). Conceptual Design of Chemical Processes. McGraw-Hill Book Company.
Marshall and Swift (2020): 2171.6
Fc = (Fd + Fp) Fm
 | C1
Heat Duty (MW) | -0.201
 | 10.72
 | 0
 | 2.81
 | 0.85
 | 2.39
Installed Cost | $8,775
 | C1
Heat Duty (MW) | -0.201
 | 10.72
 | 0
 | 2.81
 | 0.85
 | 2.39
Installed Cost | $8,775

## Slide 25: Utility costs-1st flowsheet
Cost reference: Table E.1-1 from James M. Douglas. (1988). Conceptual Design of Chemical Processes. McGraw-Hill Book Company. Assume T cooling water=15℃ at 1 bar (other operational pressure will be accustomed according to Thermodynamic T-S diagram), Cp=4.2 kJ/K.mol (water) and 1.87 kJ/K.mol (steam)
Equipment | Utility | Parameter |  | 
 |  | Price | Amount (gal/yr or lb/yr) | Cost (USD/year)
Column 1 | Cooling water | (USD/gal) | 62,946,852 | 
Column 2 |  |  | 11,758,291 | 
Column 3 |  |  | 78,431,682 | 
Reactor 2,4 |  |  | 32,186,236 | 
Reactor 3,5 |  |  | 2,804,702 | 
Column 2 | Steam | (USD/lb) | 865,740,563 | 
Column 3 |  |  | 2,352,767,663 | 
Reactor 1 |  | (USD/lb) | 3,197,858,400 | 
Pump | Electricity |  |  | 
Total: USD/yr
Total:
USD/yr

## Slide 26: Utility costs-2nd flowsheet
Equipment | Utility | Parameter |  | 
 |  | Price | Amount (gal/yr or lb/yr) | Cost (USD/year)
Flash 1 | Cooling water | (USD/gal) | 102,022,395 | 
Cooler |  |  | 907,883 | 
Column |  |  | 179,887,802 | 
Reactor 2,4 |  |  | 28,293,924 | 
Reactor 3,5 |  |  | 5,004,460 | 
Column | Steam | (USD/lb) | 1,832,366,268 | 
Reactor 1 |  | (USD/lb) | 8,577,495,772 | 
Pump | Electricity |  |  | 
Total: USD/yr
Total:
USD/yr
Cost reference: Table E.1-1 from James M. Douglas. (1988). Conceptual Design of Chemical Processes. McGraw-Hill Book Company. Assume T cooling water=15℃ at 1 bar (other operational pressure will be accustomed according to Thermodynamic T-S diagram), Cp=4.2 kJ/K.mol (water) and 1.87 kJ/K.mol (steam)

## Slide 27: Labor Cost
NOL =
NOL: # of operator per shift
P: # of particulate solids handling
Nnp: # of non-particulate solids of handling
P = 1
= 3
NOL =
NOL = 30 operators
Minimum monthly wage:
NT 35,000/person 1 month salary = $1,268 / person
1 year wage:
$14,582 x 30 = $437,460/year

## Slide 28: Total Calculation
$/Year | Flowsheet 1 | Flowsheet 2
Purchase Cost | $1,014,705 | $793,870
Installed Cost | $1,882,115 | $1,325,381
Utilities | $13,247,673 | $24,734,910
Onsite Cost | $16,144,493 | $26,854,161
Offsite Cost | $48,433,479 | $80,562,483
Start-up Cost | $8,072,247 | $13,427,081
Working Capital | $5,715,151 | $9,506,373
Fixed Capital Investment | $80,722,465 | $134,270,805
Total Capital Investment | $38,101,004 | $63,375,819
Offsite Cost =
Start-up costs = 0.1 FCI
Working capital = 0.15 TCI
Fixed capital investment =
Total capital investment

## Slide 29: Profitability Calculation
$/Year | Flowsheet 1 | Flowsheet 2
Revenue | $674,300,000 | $652,100,000
Total Production Cost | $57,000,972 | $61,184,836
Gross profit before tax | $617,299,028 | $590,915,164
Depreciation | $2,922,153 | $4,860,603
Profit after tax | $509,932,806 | $486,425,286
Cash Flows | $512,924,959 | $491,285,889
Tax Taiwan: 17%
Revenue =
Total production cost
Gross Profit before taxes =
Depreciation =
Profit after taxes = (
Cash flow

## Slide 30: Return of Investment
Annual percent return on investment before taxes
rb =
Annual percent return on investment after taxes
ra =
 | Flowsheet 1 | Flowsheet 2
rb | 1620 | 932.4
ra | 1338.4 | 767.53
Pay Out Time (year) =
Flowsheet 1 | 0.1731
Flowsheet 2 | 0.3
Pay Out Time

## Slide 31: DCFROR (Discounted Cash Flow Rate of Return)

## Slide 32
 | Flowsheet 1 |  | Flowsheet 2 | 
 | i= | 0.876665 | i= | 0.691084
 | Investment | Discount Factor | Investment | Discount Factor
Year 4 | 8,072,247 | 12.4036 | 13,427,081 | 8.1783
Year 3 | 32,288,986 | 6.6094 | 53,708,322 | 4.8361
Year 2 | 32,288,986 | 3.5219 | 53,708,322 | 2.8598
Year 1 | 8,072,247 | 1.8767 | 13,427,081 | 1.6911
Working Capital | 5,715,151 | 1 | 9,506,373 | 1
Start-Up Cost | 8,072,247 | 1 | 13,427,081 | 1
PV Investment |  | 456,188,661 |  | 568,782,044
 | Cash Flow |  | Cash Flow | 
Year 1 | 307,712,975 | 0.5329 | 294,771,533 | 0.5913
Year 2 | 461,569,463 | 0.2839 | 442,157,300 | 0.3497
Year 3 | 487,212,211 | 0.1513 | 466,721,595 | 0.2068
Year 4 | 512,854,959 | 0.0806 | 491,285,889 | 0.1222
Year 5 | 512,854,959 | 0.043 | 491,285,889 | 0.0723
Year 6 | 512,854,959 | 0.0229 | 491,285,889 | 0.0428
Year 7 | 512,854,959 | 0.0122 | 491,285,889 | 0.0253
Year 8 | 512,854,959 | 0.0065 | 491,285,889 | 0.0149
Year 9 | 512,854,959 | 0.0035 | 491,285,889 | 0.0088
Year 10 | 512,854,959 | 0.0018 | 491,285,889 | 0.0052
Working Capital | 5,715,151 | 0.0018 | 9,506,373 | 0.0052
Salvage Value | 2,421,674 | 0.0018 | 4,028,124 | 0.0052
PV Return |  | 456,188,661 |  | 568,781,081

## Slide 33: Conclusion

## Slide 34: Comparison of Design 1 & 2
Design Point of View
Economic Point of View
 | Flowsheet 1 | Flowsheet 2
Total Capital Investment | $38,101,004 | $63,375,819
Total Production Cost | $57,000,972 | $61,184,836
ROI (rb,ra) | 1620, 1338.4 | 932.4, 767.53
Payout Time | 0.1731 | 0.3
DCFROR | 87.67% | 69.11%
 | Flowsheet 1 | Flowsheet 2
Reactor Volume | 1597.86 L (CSTR) | 254.38 L (CSTR)
 | 4586.98 (PFRs) | 4586.98 (PFRs)
Distillation Tower | Column 1: 16 stages | 30 stages
 | Column 2: 21 stages | 
 | Column 3: 25 stages | 
EG produced (ton/yr) | 6,872,400 (100 w%) | 7,286,400 (99w%)

## Slide 35: Thank you